## Slide 1: Fundamentals of Computer Networks and Management
Atul Kahate

## Slide 2: Sessions 1 and 2

## Slide 3: Introduction to Communication System
A communication system is a set of interconnected components or devices that enable the transmission, reception, and exchange of information between two or more parties

## Slide 4: Components of a Data Communication System
Source: The source generates the information to be transmitted, which can be in the form of speech, data, video, or any other type of message
Transmitter: The transmitter processes the information from the source and converts it into a suitable form for transmission, e.g. by modulation (changing the signal's characteristics) and amplification
Channel: The channel is the physical or logical medium through which the signal travels (wired - copper or fiber-optic cables or wireless - radio waves, microwaves, or infrared)
Receiver: The receiver receives the transmitted signal and converts it back into a form that can be understood by the destination, e.g. by demodulation and signal processing
Destination: The destination is the recipient of the transmitted information, e.g. a person, another device, or a computer system

## Slide 5: Issues in Computer Networking
Bandwidth Limitations
Latency
Packet loss
Network congestion
Security threats
Data privacy
Scalability
Interoperability
Network management
Quality of Service

## Slide 6: Scale and Network Types

## Slide 7: Local Area Network (LAN)
Local Area Network (LAN): A privately owned network that operates within a single building like a home, office or factory
Wireless LANs: In these systems, every computer has a wireless modem and an antenna that it uses to communicate with other computers
  An access point or base station controls the network
  IEEE 802.11 standard (also called WiFi) describes this

## Slide 8: Network Topology
Network Topology represents a network arrangement consisting of several nodes

## Slide 9: Bus Topology
All the nodes are connected to a common wire, called as bus
Simple and cost-effective, but all depends on a single cable, not fast

## Slide 10: Ring Topology
One computer is connected to the next, and so on, to complete a ring
A transmitting computer needs to have a token, before transmitting
Inexpensive, Tough to add or remove nodes, One node crashing can disconnect the whole network

## Slide 11: Star Topology
Each device is connected to a central hub
All communication goes through the hub only
Simple, too much of dependence on the hub, but the hub can be upgraded easily, Easy to troubleshoot, Cost is high

## Slide 12: Mesh Topology
All nodes are connected to each other
Point-to-point connection, so for n nodes: links
Very robust, Easy to diagnose errors, Privacy and security are better, Costly, Too much of wiring

## Slide 13: Tree Topology
Nodes are connected hierarchically, ultimately connecting to the top node, called as the root node
Has at least three levels of hierarchy
Easy to expand and manage, debug
Expensive, lot of cabling

## Slide 14: Network Interface Card (NIC)

## Slide 15: Transmission media

## Slide 16: Transmission media

## Slide 17: Transmission Media
Transmission medium: Carries information from a source to a destination
Guided media (Wired) include twisted-pair cable (uses electric current), coaxial cable (uses electric current), fiber-optic cable (uses light)
Unguided medium (Wireless) is air

## Slide 18: Twisted-pair cable
Consists of two copper wires
Two types
  Unshielded twisted-pair (UTP)
  Shielded twisted-pair (STP)
Used in telephone networks

## Slide 19: Coaxial cables
Coaxial cable (or coax) carries signals of higher frequency ranges than those in twisted-pair cable
Instead of having two wires, coax has a single copper wire
Usage: Telephone, Cable TV, LAN

## Slide 20: Fiber-optic cable
Made of glass or plastic and transmits signals in the form of light
Modern Ethernet is fiber optic-based

## Slide 21: Unguided media
Use electromagnetic waves – no wire is needed
Also called as wireless communication
Signals are normally broadcast through free space and thus are available to anyone who has a device capable of receiving them
The part of the electromagnetic spectrum, ranging from 3 kHz to 900 THz is used for wireless communication.

## Slide 22: Ethernet
Most popular LAN technology
Earlier, we also had Token Ring, Token Bus, etc
Ethernet generations
  Standard Ethernet (10 Mbps)
  Fast Ethernet (100 Mbps)
  Gigabit Ethernet (1 Gbps)
  10 Gigabit Ethernet (10 Gbps)

## Slide 23: Earlier Ethernet – Classic Ethernet
Carrier sense multiple access with collision detection (CSMA/CD) technique was used
Allow any host to send data
If two hosts transmit at the same time, collision happens
They recover using CSMA/CD

## Slide 24: CSMA/CD

## Slide 25: Modern Ethernet: Switched Ethernet
Devices called switches are used to connect different computers
Classic Ethernet is the original form and ran at rates from 3 to 10 Mbps
Switched Ethernet
  Fast Ethernet: 100 Mbps
  Gigabit Ethernet: 1000 Mbps (1 Gbps)
  10 Gigabit Ethernet: 10,000 Mbps (10 Gbps)
In practice, only switched Ethernet is used nowadays

## Slide 26: Switched Ethernet
Hosts connect into switches, and switches connect to each other
Ethernet switch

## Slide 27: LAN – Earlier and Now

## Slide 28: Wide Area Network (WAN)
A Wide Area Network (WAN) spans a large geographical area, often a country or continent
Example: Two LANs can be connected to form a WAN

## Slide 29: Sessions 3 and 4

## Slide 30: Protocol
Communication between two people or two devices needs to follow some protocol
A protocol is a set of rules that governs communication
For example, in a face-to-face communication between two persons, there is a set of implicit rules in each culture that define how two persons should start the communication, how to continue the communication, and how to end the communication

## Slide 31: Network Software
Network software uses a protocol stack
A protocol stack contains many layers or levels
Each layer provides some services to the layer above it
Each layer hides complexity of its work from the layer above it
Creates a protocol hierarchy

## Slide 32: Protocol Hierarchy Example

## Slide 33: OSI
Open Systems Interconnection
Good in theory, not used in practice
Contains 7 layers
Sometimes also called ISO/OSI

## Slide 34
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Layers in OSI
Notes: 34

## Slide 35: An Exchange using the OSI Model

## Slide 36: The Application Layer

## Slide 37: Application Layer
Provides an “application view” to a network (e.g. email, file transmission)
Example: Hypertext Transfer Protocol (HTTP) is used to access Web pages
Encapsulation begins here
Other examples: Email (SMTP), File transfers (FTP), Querying domain names (DNS)

## Slide 38: The Presentation Layer

## Slide 39: Presentation Layer
Translation: Use of a common format to take care of differences (encoding, number representation etc)
Encryption: To achieve confidentiality or privacy
Compression: Reduces the number of bits needed to be transmitted

## Slide 40: The Session Layer

## Slide 41: Session Layer
Manages the session between applications
Example: Between browser of the source computer and server of the destination computer

## Slide 42: The Transport Layer

## Slide 43: Transport Layer
Identifies the application on the destination computer using port numbers
Example: One server, multiple applications

## Slide 44: Port Numbers
Port number is a 16-bit value, so it can store a number between 0 and 65,535
Port Number Range | Where used? | Called as
0-1023 | Server | Well-known ports
1024-49151 | Client | Temporary/Ephemeral
49152-65535 | NA | Dynamic, Usage-based

## Slide 45: The Network Layer

## Slide 46: Network Layer
Physical/MAC addresses are defined by data link layer to take care of addressing inside the same network
If a packet has to travel across a network to another network, physical addressing will not work
Hence, a universal address or a logical address is required. This is done at the network layer
This is the IP address

## Slide 47: The Data Link Layer

## Slide 48: Data Link Layer
Responsible for delivery of packets between two hosts connected to the same physical network (hop-to-hop – see next slide)
  Cannot work across networks
Uses frames
Physical addressing: Adding sender’s and receiver’s physical addresses (also called MAC addresses) to the frame header
LAN/WAN operates at this layer (e.g. Ethernet or WiFi)
What if we know the IP address of a computer but do not know its MAC address?
  Use Address Resolution Protocol (ARP)

## Slide 49: The Physical Layer

## Slide 50: Physical Layer Functions
Carries the data (0s and 1s) in the form of signals
Signals can be electric, optical, or wireless

## Slide 51: Physical and Logical Address
Each computer on the Internet has two addresses:
Physical address/MAC address/Hardware address
  Fixed address, hardcoded on the Network Interface Card (NIC)
  Different for different network type (e.g. Ethernet card, WiFi card)
  Useful within or inside a network only
Logical address/IP address/Virtual address
  Exists in software
  Given by the network provider or your organization (usually temporary)
  Useful outside a network (e.g. to reach another computer on the Internet, anywhere in the world)

## Slide 52: Example

## Slide 53: Example
Suppose we have used our web browser to access a web page located on our company’s web server
Consider that the following are the details of the two computers
Computer | IP Address | MAC Address | Port Number
Web server | 192.168.5.1 | 5-5-5-5-5-5 | TCP 80
Laptop | 192.168.5.2 | 6-6-6-6-6-6 | TCP 5091

## Slide 54: How will the Web Server Respond?
Layer 7 obtains the data in the form of the HTML document.
Layer 6 adds information about the formatting.
Layer 5 adds information required to create a session between the web server and the web browser on the laptop.
Layer 4 adds the transport protocol and the source and destination port numbers, in this case TCP (it's a unicast) and port 80 (HTTP).
Layer 3 adds the source and destination IP addresses, in this case a source of 192.168.5.1 and a destination of 192.168.5.2.
Layer 2 learns the destination MAC address and adds the source and destination MAC addresses, in this case, a source of 5-5-5-5-5-5 and destination of 6-6-6-6-6-6.
Layer 1 converts the entire package into bits and sends it across the network to the laptop.

## Slide 55: How will the Laptop Handle this?
Layer 1 receives the bits in electrical format, converts them to be read by layer 2, and hands them to layer 2.
Layer 2 examines the destination MAC address to see whether it is addressed to it, sees the MAC address of 6-6-6-6-6 (its own), drops that part of the transmission, and hands the remaining data to layer 3.
Layer 3 examines the destination IP address to ensure that it is its own (192. 168.5.2), drops that part, and hands the rest of the package to layer 4.
Layer 4 examines the destination port number (port 5091), alerts the browser that HTTP data is coming in, drops that part, and hands the rest of the package to layer 5.
Layer 5 uses the information that was placed on this layer by the web server to create the session between the web server and the web browser and then hands the rest of the information to layer 6.
Layer 6 performs any format translation that may be required and hands the remaining data (the HTML document) to layer 7.
The layer 7 application (the web browser) receives the HTML document and opens the document in the browser window.

## Slide 56: TCP/IP

## Slide 57: Basics of TCP/IP
The TCP/IP protocol suite was developed prior to the OSI model
Therefore, the layers in the TCP/IP protocol suite do not match exactly with those in the OSI model
The original TCP/IP protocol suite was defined as four software layers built upon the hardware
Sometimes TCP/IP is thought of as a five-layer model with the layers named similarly to the ones in the OSI model

## Slide 58: OSI versus TCP/IP
When we compare the two models, we find that two layers, session and presentation, are missing from the TCP/IP protocol suite
These two layers were not added to the TCP/IP protocol suite after the publication of the OSI model
The application layer in the suite is usually considered to be the combination of three layers in the OSI model
See diagram on the next slide

## Slide 59: OSI versus TCP/IP

## Slide 60: Protocols within Each TCP/IP Layer

## Slide 61: Transport Layer Protocols
Transmission Control Protocol (TCP)
  Reliable protocol
  Guaranteed delivery
  Uses connections, acknowledgements
  Used for text-based data
User Datagram Protocol (UDP)
  Unreliable protocol
  No guarantee of delivery
  No connections, no acknowledgements
  Useful for audio, video or wherever we need speed but not guarantee

## Slide 62: TCP – Connection Management
Connection establishment
Data transfer
Connection termination

## Slide 63: UDP
No connection
No acknowledgement
No retransmissions in the case of errors