## Slide 1: Session 8-10: Network Devices – Hub, Switch, and Router

## Slide 2: Networking devices
Inside a network
  Hub: Older device
  Switch: Modern device
To connect different networks
  Router

## Slide 3: Hub
Earlier, hubs were used as connection devices in Ethernet
Hub is a dumb device, works only at the physical layer (Layer 1)
So, it does not know about MAC addresses, and hence floods out all the ports
All devices that use the same physical media and listen to each frame are considered to be in the same collision domain

## Slide 4: Switch
Hubs are obsolete
Switch is an intelligent device – can filter traffic
Example
  If a hub connects two branches of a network, it will flood both the branches for every received frame
  A switch will check whether it should send it to the other branch of the network by comparing addresses, as discussed shortly

## Slide 5: Switching Example – 1
Each switch maintains a mapping table

## Slide 6: Switching Example – 2
Host 1.1.1 sends a frame to host 2.2.2
Switch sees the frame and updates its mapping table
The switch does not know where 2.2.2 is, so it floods out the frame
`

## Slide 7: Switching Example – 3
Suppose host 2.2.2 sends a reply to 1.1.1
Switch sees the frame and updates its mapping table
The switch will send the frame only to 1.1.1

## Slide 8: Router
A router works at layer 3 (network layer) and uses IP addresses to decide where to deliver packets
Remember: A switch works at layer 2 (data link layer) and uses MAC addresses to decide where to deliver packets
Device | Layer | Uses
Router | 3 (Network) | IP addresses
Switch | 2 (Data link) | MAC addresses

## Slide 9: Routing
Routing means taking a packet from one device and sending it through the network to another device on a different network
Switching means taking a packet from one device and sending it through the network to another device on the same network
A switch can be used for sending traffic inside a network
For sending traffic outside a network we need a router

## Slide 10: Routing Example
Host A and B are on different networks
On a command prompt, the user types ping 172.16.20.2
A packet is generated on the Host A machine using the Internet Protocol (IP)
Host A sends this packet to the router
The router opens the packet and understands that the destination host B is not on the same network
Router forwards the packet to host B
Note: Several additional steps are needed for this, which are not described here for simplicity
B

## Slide 11: Routing Table
To perform routing, a router needs to build a routing table – Initial state

## Slide 12: Routing Table after it is Updated
Called as converged routing table

## Slide 13: Hubs versus Switches versus Routers
Hub | Switch | Router
Operates at layer 1 (Physical layer) | Operates at layer 2 (Data link layer) | Operates at layer 3 (Network layer)
Works inside a LAN | Works inside a LAN | Works across networks
Generally works only for Ethernet | Generally works only for Ethernet | Supports Ethernet, ISDN, ADSL, etc
Has many ports | Has more ports | Has less ports
A dumb device – floods out all the ports; so does not know about MAC or IP addresses | Works with MAC addresses | Woks with IP addresses

## Slide 14: Understanding Routing
Consider a passenger traveling from Pune to Sioux Falls, USA
Hop Number | From | To | Passenger’s View
1 | Pune | Mumbai | Pune-Sioux Falls
2 | Mumbai | San Francisco | Pune-Sioux Falls
3 | San Francisco | Chicago | Pune-Sioux Falls
4 | Chicago | Sioux Falls | Pune-Sioux Falls
Pune
Mumbai
San Francisco
Chicago
Sioux Falls

## Slide 15: Understanding Routing
Consider a datagram/packet going from computer A to computer B
R1
R2
R3
A
B
 | Data Link Layer | View | 
Hop Number | From | To | IP View
1 | A | R1 | A-B
2 | R1 | R2 | A-B
3 | R2 | R3 | A-B
4 | R3 | B | A-B

## Slide 16: MAC Addresses and LAN

## Slide 17: IP Addresses and the Internet

## Slide 18: Sessions 6 and 7: IP Addressing and Routing

## Slide 19: IP Address
An IP address has two parts:
  Network Id: Identifies which network it belongs to
  Host Id: On a given network, what is the host number
Examples:
This notation is called as dotted decimal notation
Some portion of the network id is reserved to indicate class of IP address
Hence, this is called as classful addressing
14.22.130.89
143.1.99.204
193.56. 78.21

## Slide 20: IP Address Classes

## Slide 21: Classful Addressing

## Slide 22: Classes – How to Determine/Remember? – Three Techniques
Look at the first few bits of the binary value of the network id
  First bit 0: Class A
  First two bits 10: class B
  First three bits 110: class C
Look at the first decimal octet/byte value of the network id
  0-127: Class A
  128-191: Class B
  192-223: Class C
Use the flow-chart on the following slide

## Slide 23
Determining Class
First bit = 0?
Second bit = 0?
Third bit = 0?
Fourth bit = 0?
Yes
Yes
Yes
Yes
No
No
No
No
Class A address
Class B address
Class C address
Class D address
Class E address
Notes: 23

## Slide 24: Dotted Decimal Notation

## Slide 25: Masking
Hide the host id part of an IP address
Retain the network id part
This is called masking (the host id part)

## Slide 26: Calculation
134.45.78.2
255.255.0.0
AND
134.45.0.0
The address whose network ID we want
Default mask for class B (since the address above is from class B)
Network ID for the address

## Slide 27: Default Mask

## Slide 28
Default Masks
Class | Mask in Binary | Mask in dotted-decimal
A | 11111111 00000000 00000000 00000000 | 255.0.0.0
B | 11111111 11111111 00000000 00000000 | 255.255.0.0
C | 11111111 11111111 11111111 00000000 | 255.255.255.0
Notes: 28

## Slide 29
Masking Examples
Given an IP address of 23.56.7.91, find the network address.
Given an IP address of 132.6.17.85, find the network address.
Notes: 29

## Slide 30: Private/Local/Internal IP Addresses
The following ranges of IP addresses are reserved as private/local/internal IP addresses, and they cannot be assigned to a computer on the Internet as a public/external IP address
Class A: 10.0.0.0 to 10.255.255.255
Class B: 172.16.0.0 to 172.31.255.255
Class C: 192.168.0.0 to 192.168.255.255