## Slide 1: Static Routing

## Slide 2: Static Routing Concept
We need to manually add routing information to the routers
Routers do not automatically create/update routing information
Easy but not efficient
Can be used for small networks

## Slide 3: Static Routing Setup
Create a ring topology
(Next slide for details)

## Slide 4: Creating the Ring Topology
Add four routers with the following details – Make sure Port is On

## Slide 5: Configuring Routes Statically
Open the first Router (R1) and in Routing, add the routes
Enter the details here and click on Add

## Slide 6: Similarly, for the Others, Add Information as Below

## Slide 7: Checking Routing Table
We can examine any router’s routing table by clicking on the search button (called Inspect) on the top left corner of the screen
and then selecting a router

## Slide 8: Testing
Add a simple PDU from the menu to any two routers and see if they can route the packet correctly or not

## Slide 9: Static Routing Using CLI
Consider four routers (Same configuration as earlier, using 172 address, instead of 192):
R1 has IP addresses 172.168.10.1 on interface F0/0 and 172.168.20.1 on interface F0/1
R2 has IP addresses 172.168.10.2 on interface F0/0 and 172.168.30.1 on interface F0/1
R3 has IP addresses 172.168.20.2 on interface F0/0 and 172.168.40.1 on interface F0/1
R4 has IP addresses 172.168.30.2 on interface F0/0 and 172.168.40.2 on interface F0/1
Write Cisco Packet Tracer commands for basic router set up, followed by static routing commands.

## Slide 10: Static Routing – R1
R1>enable
R1#configure terminal
R1(config)#hostname R1
R1(config)#interface FastEthernet0/0
R1(config-if)#ip address 172.168.10.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
R1(config)#interface FastEthernet0/1
R1(config-if)#ip address 172.168.20.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
R1(config)#exit
R1>enable
R1#configure terminal
R1(config)#ip route 172.168.30.0 255.255.255.0 172.168.20.2
R1(config)#ip route 172.168.40.0 255.255.255.0 172.168.20.2
R1(config)#exit
Basic router set up
Static routing

## Slide 11: Static Routing – R2
R2>enable
R2#configure terminal
R2(config)#hostname R2
R2(config)#interface FastEthernet0/0
R2(config-if)#ip address 172.168.10.2 255.255.255.0
R2(config-if)#no shutdown
R2(config-if)#exit
R2(config)#interface FastEthernet0/1
R2(config-if)#ip address 172.168.30.1 255.255.255.0
R2(config-if)#no shutdown
R2(config-if)#exit
R2(config)#exit
R2>enable
R2#configure terminal
R2(config)#ip route 172.168.20.0 255.255.255.0 172.168.10.1
R2(config)#ip route 172.168.40.0 255.255.255.0 172.168.30.2
R2(config)#exit

## Slide 12: Static Routing – R3
R3>enable
R3#configure terminal
R3(config)#hostname R3
R3(config)#interface FastEthernet0/0
R3(config-if)#ip address 172.168.20.2 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit
R3(config)#interface FastEthernet0/1
R3(config-if)#ip address 172.168.40.1 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit
R3(config)#exit
R3>enable
R3#configure terminal
R3(config)#ip route 172.168.10.0 255.255.255.0 172.168.20.1
R3(config)#ip route 172.168.30.0 255.255.255.0 172.168.40.2
R3(config)#exit

## Slide 13: Static Routing – R4
R4>enable
R4#configure terminal
R4(config)#hostname R4
R4(config)#interface FastEthernet0/0
R4(config-if)#ip address 172.168.30.2 255.255.255.0
R4(config-if)#no shutdown
R4(config-if)#exit
R4(config)#interface FastEthernet0/1
R4(config-if)#ip address 172.168.40.2 255.255.255.0
R4(config-if)#no shutdown
R4(config-if)#exit
R4(config)#exit
R4>enable
R4#configure terminal
R4(config)#ip route 172.168.10.0 255.255.255.0 172.168.30.1
R4(config)#ip route 172.168.20.0 255.255.255.0 172.168.40.1
R4(config)#exit

## Slide 14: Dynamic Routing

## Slide 15: Dynamic Routing
Routing Information Protocol (RIP) is used by routers to exchange information so as to build routing tables
We do not have to add routing information statically now
Routers automatically do this

## Slide 16: Configuring RIP
1. Create the same four-router topology we used previously and assign the same IP addresses through the Config tab.

## Slide 17: Configuring RIP
2. Click on RIP. This is very easy. Each router now requires only the Network IP of its own interfaces, as shown in the following screenshot:
Full list – next slide

## Slide 18: Network Addresses for RIP Configuration

## Slide 19: Test using the PDU
Same as before

## Slide 20: RIP Dynamic Routing Using CLI
Consider four routers:
R1 has IP addresses 172.168.10.1 on interface F0/0 and 172.168.20.1 on interface F0/1
R2 has IP addresses 172.168.10.2 on interface F0/0 and 172.168.30.1 on interface F0/1
R3 has IP addresses 172.168.20.2 on interface F0/0 and 172.168.40.1 on interface F0/1
R4 has IP addresses 172.168.30.2 on interface F0/0 and 172.168.40.2 on interface F0/1
Write Cisco Packet Tracer commands for basic router set up, followed by static routing commands.

## Slide 21: Dynamic Routing using RIP - R1
R1>enable
R1#configure terminal
R1(config)#hostname R1
R1(config)#interface FastEthernet0/0
R1(config-if)#ip address 172.168.10.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
R1(config)#interface FastEthernet0/1
R1(config-if)#ip address 172.168.20.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
R1(config)#exit
R1>enable
R1#configure terminal
R1(config)#router rip
R1(config-router)#version 2
R1(config-router)#network 172.168.10.0
R1(config-router)#network 172.168.20.0
R1(config-router)#exit
R1(config)#exit
Basic router set up
Dynamic routing using RIP

## Slide 22: Dynamic Routing using RIP – R2
R2>enable
R2#configure terminal
R2(config)#hostname R2
R2(config)#interface FastEthernet0/0
R2(config-if)#ip address 172.168.10.2 255.255.255.0
R2(config-if)#no shutdown
R2(config-if)#exit
R2(config)#interface FastEthernet0/1
R2(config-if)#ip address 172.168.30.1 255.255.255.0
R2(config-if)#no shutdown
R2(config-if)#exit
R2(config)#exit
R2>enable
R2#configure terminal
R2(config)#router rip
R2(config-router)#version 2
R2(config-router)#network 172.168.10.0
R2(config-router)#network 172.168.30.0
R2(config-router)#exit
R2(config)#exit

## Slide 23: Dynamic Routing using RIP – R3
R3>enable
R3#configure terminal
R3(config)#hostname R3
R3(config)#interface FastEthernet0/0
R3(config-if)#ip address 172.168.20.2 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit
R3(config)#interface FastEthernet0/1
R3(config-if)#ip address 172.168.40.1 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit
R3(config)#exit
R3>enable
R3#configure terminal
R3(config)#router rip
R3(config-router)#version 2
R3(config-router)#network 172.168.20.0
R3(config-router)#network 172.168.40.0
R3(config-router)#exit
R3(config)#exit

## Slide 24: Dynamic Routing using RIP – R4
R4>enable
R4#configure terminal
R4(config)#hostname R4
R4(config)#interface FastEthernet0/0
R4(config-if)#ip address 172.168.30.2 255.255.255.0
R4(config-if)#no shutdown
R4(config-if)#exit
R4(config)#interface FastEthernet0/1
R4(config-if)#ip address 172.168.40.2 255.255.255.0
R4(config-if)#no shutdown
R4(config-if)#exit
R4(config)#exit
R4>enable
R4#configure terminal
R4(config)#router rip
R4(config-router)#version 2
R4(config-router)#network 172.168.30.0
R4(config-router)#network 172.168.40.0
R4(config-router)#exit
R4(config)#exit

## Slide 25: Dynamic Routing using EIGRP

## Slide 26: EIGRP Configuration
Consider four routers:
R1 has IP addresses 172.168.10.1 on interface F0/0 and 172.168.20.1 on interface F0/1
R2 has IP addresses 172.168.10.2 on interface F0/0 and 172.168.30.1 on interface F0/1
R3 has IP addresses 172.168.20.2 on interface F0/0 and 172.168.40.1 on interface F0/1
R4 has IP addresses 172.168.30.2 on interface F0/0 and 172.168.40.2 on interface F0/1
Write Cisco Packet Tracer commands for the basic router set up followed by EIGRP commands for each router.

## Slide 27: EIGRP on R1
R1>enable
R1#configure terminal
R1(config)#hostname R1
R1(config)#interface FastEthernet0/0
R1(config-if)#ip address 172.168.10.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
R1(config)#interface FastEthernet0/1
R1(config-if)#ip address 172.168.20.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
R1(config)#exit
R1>enable
R1#configure terminal
R1(config)#router eigrp 100
R1(config-router)#network 172.168.10.0
R1(config-router)#network 172.168.20.0
R1(config-router)#exit
R1(config)#exit

## Slide 28: EIGRP on R2
R2>enable
R2#configure terminal
R2(config)#hostname R2
R2(config)#interface FastEthernet0/0
R2(config-if)#ip address 172.168.10.2 255.255.255.0
R2(config-if)#no shutdown
R2(config-if)#exit
R2(config)#interface FastEthernet0/1
R2(config-if)#ip address 172.168.30.1 255.255.255.0
R2(config-if)#no shutdown
R2(config-if)#exit
R2(config)#exit
R2>enable
R2#configure terminal
R2(config)#router eigrp 100
R2(config-router)#network 172.168.10.0
R2(config-router)#network 172.168.30.0
R2(config-router)#exit
R2(config)#exit

## Slide 29: EIGRP on R3
R3>enable
R3#configure terminal
R3(config)#hostname R3
R3(config)#interface FastEthernet0/0
R3(config-if)#ip address 172.168.20.2 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit
R3(config)#interface FastEthernet0/1
R3(config-if)#ip address 172.168.40.1 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit
R3(config)#exit
R3>enable
R3#configure terminal
R3(config)#router eigrp 100
R3(config-router)#network 172.168.20.0
R3(config-router)#network 172.168.40.0
R3(config-router)#exit
R3(config)#exit

## Slide 30: EIGRP on R4
R4>enable
R4#configure terminal
R4(config)#hostname R4
R4(config)#interface FastEthernet0/0
R4(config-if)#ip address 172.168.30.2 255.255.255.0
R4(config-if)#no shutdown
R4(config-if)#exit
R4(config)#interface FastEthernet0/1
R4(config-if)#ip address 172.168.40.2 255.255.255.0
R4(config-if)#no shutdown
R4(config-if)#exit
R4(config)#exit
R4>enable
R4#configure terminal
R4(config)#router eigrp 100
R4(config-router)#network 172.168.30.0
R4(config-router)#network 172.168.40.0
R4(config-router)#exit
R4(config)#exit

## Slide 31: Dynamic Routing using OSPF

## Slide 32: Dynamic Routing OSPF
Consider four routers:
R1 has IP addresses 172.168.10.1 on interface F0/0 and 172.168.20.1 on interface F0/1
R2 has IP addresses 172.168.10.2 on interface F0/0 and 172.168.30.1 on interface F0/1
R3 has IP addresses 172.168.20.2 on interface F0/0 and 172.168.40.1 on interface F0/1
R4 has IP addresses 172.168.30.2 on interface F0/0 and 172.168.40.2 on interface F0/1
Write Cisco Packet Tracer commands for the basic router set up followed by OSPF commands for each router.

## Slide 33: OSPF – R1
R1>enable
R1#configure terminal
R1(config)#hostname R1
R1(config)#interface FastEthernet0/0
R1(config-if)#ip address 172.168.10.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
R1(config)#interface FastEthernet0/1
R1(config-if)#ip address 172.168.20.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#exit
R1(config)#exit
R1>enable
R1#configure terminal
R1(config)#router ospf 1
R1(config-router)#network 172.168.10.0 0.0.0.255 area 0
R1(config-router)#network 172.168.20.0 0.0.0.255 area 0
R1(config-router)#exit
R1(config)#exit

## Slide 34: OSPF – R2
R2>enable
R2#configure terminal
R2(config)#hostname R2
R2(config)#interface FastEthernet0/0
R2(config-if)#ip address 172.168.10.2 255.255.255.0
R2(config-if)#no shutdown
R2(config-if)#exit
R2(config)#interface FastEthernet0/1
R2(config-if)#ip address 172.168.30.1 255.255.255.0
R2(config-if)#no shutdown
R2(config-if)#exit
R2(config)#exit
R2>enable
R2#configure terminal
R2(config)#router ospf 1
R2(config-router)#network 172.168.10.0 0.0.0.255 area 0
R2(config-router)#network 172.168.30.0 0.0.0.255 area 0
R2(config-router)#exit
R2(config)#exit

## Slide 35: OSPF – R3
R3>enable
R3#configure terminal
R3(config)#hostname R3
R3(config)#interface FastEthernet0/0
R3(config-if)#ip address 172.168.20.2 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit
R3(config)#interface FastEthernet0/1
R3(config-if)#ip address 172.168.40.1 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit
R3(config)#exit
R3>enable
R3#configure terminal
R3(config)#router ospf 1
R3(config-router)#network 172.168.20.0 0.0.0.255 area 0
R3(config-router)#network 172.168.40.0 0.0.0.255 area 0
R3(config-router)#exit
R3(config)#exit

## Slide 36: OSPF – R4
R4>enable
R4#configure terminal
R4(config)#hostname R4
R4(config)#interface FastEthernet0/0
R4(config-if)#ip address 172.168.30.2 255.255.255.0
R4(config-if)#no shutdown
R4(config-if)#exit
R4(config)#interface FastEthernet0/1
R4(config-if)#ip address 172.168.40.2 255.255.255.0
R4(config-if)#no shutdown
R4(config-if)#exit
R4(config)#exit
R4>enable
R4#configure terminal
R4(config)#router ospf 1
R4(config-router)#network 172.168.30.0 0.0.0.255 area 0
R4(config-router)#network 172.168.40.0 0.0.0.255 area 0
R4(config-router)#exit
R4(config)#exit